## Slide 1: Appalachian storage Hub (ASH) project
Semi-Annual Meeting
March 14, 2017
WVU Erickson Alumni Center

## Slide 2
Strategy 2: stratigraphic correlation
Kyle Metz – Energy Resources Group, Ohio Department of Natural Resources – Division of Geological Survey
Michael Solis - ODNR
Gary Daft - WVGES
Eric Lewis - WVGES
Kristin Carter – PAGS

## Slide 3: ASH Project
Strategy 2 – Stratigraphic Correlation of Key Units
Challenge – over 200 individual named formations. Need to alias formations and correct for state-line ‘faults’ / jumped correlations to provide a consistent set of maps for the nine intervals of interest within the AOI.
  Identify formations of value and their lateral equivalents.
  Extend correlations into areas where well logs are present but tops are missing.
Formations
Number of wells with Formation Picked
Formation top distribution input into study
Formations
Number of wells with Formation Picked
Formation top distribution after aliasing/regional correlations
3907 wells with tops

## Slide 4
Strategy 2 – stratigraphic correlation
Mississippian – Devonian : (Greenbrier, Keener to Berea, Upper Devonian Sands)
Greenbrier/Big Injun is difficult to correlate and map in OH due to unconformities and lack of logs over interval
Berea is more well developed into OH
Venango, Bradford, and Elk are more well developed in PA & WV due to proximity to catskill delta
Greenbriar – 218 wells
Big Injun – 1170 wells
Berea – 1169 wells
Venango – 543 wells
Bradford – 477 wells
Elk – 531 wells
W
E
W
E

## Slide 5
Strategy 2 – stratigraphic correlation
Mississippian – Devonian : Greenbrier
From Rice & Schwietering, 1988
From Rice & Schwietering, 1988
Greenbrier subcrop sub parallel to Ohio River. Some erosional remnants complicate contour mapping of interval.

## Slide 6
Most productive Lower Miss sandstone in basin.
Discovered in 1886.
Fluvial channel to distributary/delta front environment of deposition.
Strategy 2 – stratigraphic correlation
Mississippian – Devonian : Big Injun
From Roen et al., 1996
From Roen et al., 1996
From Roen et al., 1996

## Slide 7
First discovered in 1860.
Diverse depositional environments from fluvial-deltaic to shallow marine and barrier beach settings.
Some stacked reservoir potential
Strategy 2 – stratigraphic correlation
Mississippian – Devonian : Berea
From Roen et al., 1996
From Roen et al., 1996
From Roen et al., 1996

## Slide 8
First discovered in 1859.
Fluvial-deltaic environment of deposition in Catskill delta complex.
Sediments shed from the Acadian Orogeny.
Multiple stacked sandstone reservoirs.
Strategy 2 – stratigraphic correlation
Mississippian – Devonian : Venango, Bradford, Elk sands
From Roen et al., 1996
From Roen et al., 1996
From Roen et al., 1996

## Slide 9
Strategy 2 – stratigraphic correlation
Devonian - Silurian: (Oriskany, Salina, Newburg, Cataract Group)
Oriskany is bound by unconformities on both top and base, so presence is spotty where thin.
Salina salt basin is centered along West Virginia panhandle.
Salina F4 salt bound on top by Salina G anhydrite (~100’ thick).
Newburg developed in southwestern WV.
Cataract Group (Clinton/Medina) is present throughout area.
S
N
Oriskany– 1033 wells
Salina F– 825 wells
Newburg– 271 wells
Cataract Group– 1052 wells
S
N

## Slide 10
First discovered in 1887.
High-energy marine, nearshore environment of deposition.
Single clean sandstone reservoir.
Strategy 2 – stratigraphic correlation
Devonian - Silurian: Oriskany
From Roen et al., 1996
From Roen et al., 1996
From Roen et al., 1996

## Slide 11
First discovered in 1939, play kicked off in 1964.
Supra-to-intertidal environment with storm influence.
Single clean sandstone reservoir.
Strategy 2 – stratigraphic correlation
Devonian - Silurian: Newburg
From Roen et al., 1996
From Roen et al., 1996
From Roen et al., 1996

## Slide 12
First discovered accidentally in 1920s.
Upper ‘Clinton’ sands are shallow marine – deltaic.
Lower ‘Medina’ sands are transgressive marine sands.
Generally low porosity. Production enhanced by fractures.
Multiple stacked laterally continuous sandstone reservoirs
Strategy 2 – stratigraphic correlation
Devonian - Silurian: Cataract Group
From Roen et al., 1996
From Roen et al., 1996
From Roen et al., 1996

## Slide 13
Strategy 2 – stratigraphic correlation
Ordovician – Rose Run
Rose Run is part of the Knox unconformity play.
Has complex mineralogy (feldspar) causing GR to read high.
Best discriminator for reservoir is porosity log.
Rose Run / Gatesburg is prohibitively deep and poorly defined in WV/PA.
Rose Run – 665 wells

## Slide 14
Strategy 2 – stratigraphic correlation
Ordovician - Cambrian: Rose Run
First discovered in 1961.
Interpreted to represent lowstand sands that were reworked during sealevel transgression.
Single Laterally continuous sandstone reservoir.
From Roen et al., 1996
From Roen et al., 1996

## Slide 15
Strategy 3: Mapping
Kyle Metz – Energy Resources Group, Ohio Department of Natural Resources – Division of Geological Survey
Michael Solis - ODNR
Mohammad Fakhari - ODNR
Gary Daft- WVGES
Kristin Carter – PAGS

## Slide 16
Greenbrier
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 100 ft
Gross Isopach Map
Apparent thickness
CI = 10 ft
Structure map from WV combined with well control to generate high-resolution map that honors preexisting structure maps and newest well tops.
Data in Ohio is questionable due to drilling/logging practices and Greenbrier subcrop location.

## Slide 17
Keener to Berea
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 100 ft
Gross Isopach Map
Apparent thickness
CI = 25 ft
Used Greenbrier structure map and isopached down to Keener-Berea top, then recontoured with well control.
Assumes concordant folding with Greebrier Limestone.
Keener/Big Injun data is questionable in Ohio due to drilling/logging practices.
Gross isopach, NOT net sand

## Slide 18
Venango
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 100 ft
Gross Isopach Map
Apparent thickness
CI = 25 ft
Used Greenbrier structure map and isopached down to Venango top, then recontoured with well control.
Assumes concordant folding with Greebrier Limestone.
Gross isopach, NOT net sand

## Slide 19
Bradford
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 100 ft
Gross Isopach Map
Apparent thickness
CI = 25 ft
Used Greenbrier structure map and isopached down to Bradford top, then recontoured with well control.
Assumes concordant folding with Greebrier Limestone.
Gross isopach, NOT net sand

## Slide 20
Elk
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 100 ft
Gross Isopach Map
Apparent thickness
CI = 25 ft
Used Greenbrier structure map and isopached down to Elk top, then recontoured with well control.
Assumes concordant folding with Greebrier Limestone.
Gross isopach, NOT net sand

## Slide 21
Oriskany
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 100 ft
Gross Isopach Map
Apparent thickness
CI = 10 ft
Combined contours from RPSEA subsurface brine injection project with latest well tops.
Combined contours from RPSEA subsurface brine injection project with latest well tops.

## Slide 22
Salina ‘F4’ Salt
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 100 ft
Net Isopach Map
Net Salt thickness
CI = 10 ft
Salina ‘F’ salt and stratigraphic equivalent top.
Net Salina ‘F4’ salt basin is centered along WV panhandle/Ohio River.
F4 salt thickness exceeds 100 feet in basin center.
F3 salt ~20 feet below could add an extra 25 – 50 feet of salt.

## Slide 23
Cataract Group
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 100 ft
Gross Isopach Map
Apparent thickness
CI = 5 ft
Combined contours from RPSEA subsurface brine injection project with latest well tops.
Combined contours from RPSEA subsurface brine injection project with latest well tops.

## Slide 24
Rose Run
Strategy 3 – Mapping of Key Intervals
Structure Map
TVDss
CI = 250 ft
Gross Isopach Map
Apparent thickness
CI = 25 ft
Combined contours from RPSEA subsurface brine injection project with latest well tops.
Little-to-no well control in deeper part of basin.
Combined contours from RPSEA subsurface brine injection project with latest well tops.
Little-to-no well control in deeper part of basin.

## Slide 25
References and Acknowledgements
Rice, C.L. and Schwietering, J.F., 1988, Fluvial Deposition in the Central Appalachian During the Early Pennsylvanian, U.S. Geological Survey Bulletin: Evolution of sedimentary basins – Appalachian Basin, QE75.B9 no. 1829A-D, pp. B1-B10.
Roen, John B., Walker, Brian J., and others, 1996, The Atlas of Major Appalachian Gas Plays: West Virginia Geological and Economic Survey, Publication V-25.
I would like to thank the ASH research team for their assistance. I would also like the thank the industry partners for their support with this project.