## Slide 1: Appalachian storage Hub (ASH) project

## Slide 2: Background
Liquids-rich Marcellus and Utica Shale production in the tri-state area of OH, PA and WV
Desire to move natural gas liquids (NGLs) from wet gas areas to industrial sites throughout the greater Appalachian region
A proposed “6-pack” pipeline from Monaca, PA to northeastern KY and Charleston, WV along the Ohio & Kanawha rivers
Subsurface storage will be a necessary component along the pipeline route

## Slide 3: Prefeasibility Study: three options for NGL storage
Solution-mined salt caverns (with/without brine takeaway)
Mined-rock caverns (carbonate rock)
Gas reservoirs (siliciclastic rock)

## Slide 4: A geologic study of the potential to build an Appalachian storage hub
Data collection and project database development
Stratigraphic correlation of key units
Mapping thickness and structure of key units
Studies of reservoir character
Develop ranking criteria
Recommendations
Project Management and Technology Transfer

## Slide 5: Geologic INTERVALS of interest
Greenbrier Limestone (>40 ft thick at depths in excess of 1,800 ft; suitable for mining)
Salina Group salts (>100-ft thick preferred; suitable for solution mining)
Keener sandstone to Berea Sandstone
Upper Devonian sandstones
Oriskany Sandstone
Clinton-Medina Group through Tuscarora Sandstone
Rose Run and Upper Sandy Member of the Gatesburg Formation
Salt caverns
Gas reservoirs
Mined-rock caverns

## Slide 6: Points to consider
Storage capacity and deliverability will ultimately depend on the NGL product(s)
Storage capacity and deliverability may require more than one field and/or more than one geologic reservoir per field
Examine all three categories of storage options, ranking sites in each
Rank the top options across categories, offering recommendations for follow-on engineering assessments

## Slide 7: Introducing the Research Team
Jessica Moore – Program Manager, Applied Oil & Gas, WVGES
Mohammad Fakhari – Energy Resources Group Supervisor, OGS
Kristin Carter – Assistant State Geologist and Economic Geology Division Manager, PAGS